## Slide 1: Ethernet Over PCI Express Presented by Kallol Biswas
NucleoDyne Systems, Inc. 19925 Stevens Creek Blvd Cupertino, CA

## Slide 2: Outline of Today’s Presentation
Overview
Highlights of PCI Express Protocol
System to System communication using PCIe ( PCI Express protocol )
Advantages and Issues
Application Areas

## Slide 3: Overview
Traditional Use model
  Ethernet devices connect two or more
  computer systems.
  PCI Express bus links motherboard
  mounted peripherals or add-in devices.
New Use Model
  PCI Express switch connects two or more
  computer systems at system bus level.

## Slide 4: Multiple Computer Systems Connected through PCIe switch
Remote system’s memory is available to local system for load/store CPU instructions and DMA operations.

## Slide 5: New Use Model A process writes to a remote process’ address space

## Slide 6: Inter process communication schemes
Direct Communication
One process read/writes information to
remote process on a different system
    No socket API is necessary
    Low latency data access
TCP/IP based Communication
  Ethernet frames are sent over PCIe Bus
Observation
  Low Latency and High Throughput
  Lower Power consumption and Low cost

## Slide 7: Highlights of PCI Express Protocol
Packet based Serial bus protocol
Point to Point, bidirectional
Effective data rate on each lane 2, 4 or 8 gbps
Layer architecture
  Software, Transaction, Data Link,
  Physical
Path based routing, globally addressable fabric
QoS support
Universal acceptance

## Slide 8: System to System Communication

## Slide 9: Two Node Communication in PIO Mode
Processor
Root Complex
DDR3
Switch
FSB
System A
Processor
Root Complex
DDR3
Switch
FSB
System B
Store r3, <address in System B’s DDR>
TLP with modified header
ACK/NACK DLLP
Header
Content of r3
ECRC
LCRC
Seq#
End
Start

## Slide 10: System to System Communication Ethernet Over PCI Express

## Slide 11: Test Results Throughput & CPU Utilization

## Slide 12: Test Result - Latency

## Slide 13: Advantages
Lower Power Consumption
  A 16 lane Gen2 switch consumes ~2.5W
Lower Cost
  Cost is around $1 per len, x8 lane device costs ~$8
Savings in ecosystem
  Lower cost for each components, clocks, connectors, cables and test equipments
Lower latency and higher throughput

## Slide 14: Issues
Length Limitation
Max External cable length is approx 5m, with optical connector max length upto 100m
Maximum number of nodes supported in
a fabric
Max number of Bus x device x func
256 x 32 x 8 = 65536 nodes, Gen3 supports much larger number

## Slide 15: Application Areas
Replacement of parallel buses like VME
(Versa Modular Eurocard bus) 9.97 Gbps over x4 PCIe switch vs 2.56 Gbps
Multi-node cluster development
NVRAM mirroring
In trading systems or banking industry

## Slide 16: www.nucleodyne.com
US System software services company
Low Level Kernel & system software
Low level device drivers for storage and
communication protocols
End to end system development
  processor customization
  system board development
  OS port or write new OS
  custom application development

## Slide 17
NucleoDyne Systems, Inc. 19925 Stevens Creek Blvd, Cupertino, CA
Thank You